Design of folded plates

Trapezoidal folded plates

Span 35m

short direction:-

3*2Mb+3Mc=-6*0.585 → 2Mb+Mc=-1.17……… (1)

For symmetrical Mc=Md

3Mb+2*6Mc+3Md=-6*(0.585+.731) → Mb+5Mc=-2.632…….. (2)

From equations 1&2 Mb= -0.358 m.t, Mc= -0.455 m.t

d = k1√M/B = 0.35 * √0.46*100000/100 = 7.5cm take ts = 8.5+1.5=10cm

As=M/k2.d = 0.46*100000/1300*8.5 = 4.16 cm2 → take 6ø10/m' as main reinforcements and 5ø10/m' as secondary reinforcements.

____________________________________________________________________________________

Longitudinal direction:

Properties of plates (span 35m)

Area = width x height

Z = 2 I / h = height3 x width /(12*(height /2) )

M = S x span2 / 8

Stress = M / Z

P1 = 0.125x2.5x0.7 + 1.5x0.60 + 0.14 =1.26 t/m'

P2 = 3.0x0.6 = 1.8t/m'

| Plate | Width (m) | Height | Area (m2) | Z (m3) | S ( t/m') | M (m.t) | Stress (t/m2) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ab | 0.125 | 0.70 | 0.0875 | 0.0102083 | 1.26 | 193 | 18906 |
| bc | 0.12 | 3.0 | 0.36 | 0.18 | 3.0 | 459.375 | 2552.1 |
| cd | 0.12 | 3.0 | 0.36 | 0.18 | 0 | 0 | 0 |

Edge shears:

Joint b:  0 + 2(Tb/A1+Tb/A2) + Tc/A2 = ½ (M1/Z1 + M2/Z2)

So, 28.41*Tb +2.78*Tc = 10729.1→10.22*Tb + Tc = 3859.4

Joint c:  Tb/A2 + 2(Tc/A2+Tc/A3) + Td/A3 = ½ (M2/Z2 + M3/Z3)

Tc = -Td

So, 2.78*Tb +5.56*Tc - 2.78*Tc  = ½ (2552.1 + 0) → Tb + Tc = 459

10.22*Tb + Tc = 3859.4

-Tb - Tc = -459

Tb = 368.8 t & Tc = 90.2 t

Stress analysis of plates

Plate ab:

Assume the height of tension zone in plate ab =0.586 m

Plate bc:

Plate cd:

Final stress diagram

Determination of longitudinal tension steel

According to final stress figure tension force in the cross section of the folded plate

T = ½ x10476 x 0.5856 x 0.25 = 766.84 t

Use steel 52  = 2t/cm2

As = 766.84/2 = 383.422 cm2 → 28ø42mm

Shear stress

Max. Shear force at diaphragms Qmax = Pb L / 2 = 1.26 * 35 / 2 = 22.05 t

Shear stress at mid height of plate ab max = ³/² Qmax / A

= 3*22.05 /2*0.0875 = 378 t/m2

Shear stress at diaphragms due to Tb = 368.8t

At top edge  = 4Tb / b L =4*368.8/0.125*35 = 337.2t/m2

At mid height /4 = 337.2 / 4 = 84.3 t/m2

Total shear stress at mid height = 378 – 84.3 = 293.7 t / m2

------------------------------------------------------------------------

Max. shear force at diaphragms Qmax = Pb L / 2 = 3 * 35 / 2 = 52.5 t

Shear stress at mid height of plate bc max = ³/² Qmax / A

= 3*52.5 /2*0.36 = 218.75 t/m2

Shear stress at diaphragms due to Tb = 368.8t

At top edge  = 4Tb / b L =4*368.8/0.12*35 = 351.2 t/m2

At mid height /4 = 351.2 / 4 = 87.81 t/m2

----------------------------------------------------------------------------

Shear stress at diaphragms due to Tc = 90.2t

At top edge  = 4Tc / b L =4*90.2/0.12*35 = 85.9 t/m2

Shear stress at mid height of plate bc due to Tc = 85.9/4 = 21.5t/m2

Total shear stress at mid height of plate bc

= 218.78 – 87.81- 21.5 = 109.5 t / m2

Reinforcement for shear:

Design of Diaphragm:

Design each diaphragm as simply supported beam supported on columns.

Distributed loads acting on the diaphragm w /m' = o. wt. of diaphragm

+distributed load /m2 acting on plates x Span/2

= 15.85*2.5*0.25/8+0.65*35/2

= 12.6 t/m'

Max. +ve Moment = 12.6*82/8 = 100.91 m.t.

Max. Shear Force = 12.6*8/2 = 50.4 t

Let the thickness of diaphragm = 25 cm

d = k1√M/b = 0.35√100.91*105/25 = 222.4 cm let d = 250 cm and t = 255 cm

As = M/k2 d = 100.91 * 105 / 2000 * 250 = 20.182 cm2 → 8 ø 18 mm

 = Q/0.87 bd = 50.4*1000/0.87*25*250 = 9.3 kg/cm2

Take 2*2 ø 18 mm as bent bars

Note:The reinforcement will cover the moment for small depth.

The bent bars will appear in the sloped depth section.

The secondary reinforcement for transfer direction resist shear stress in plates.

Design of Triangular Folded Plates (Span 20m)

Slab action :

d = k1√M/b = 0.35√0.39*105/100 = 6.91 cm let d = 8.50 cm and t = 10 cm

As = M/k2 d = 0.39 * 105 / 2000 * 8.5 = 2.29 cm2 → 5 ø 10 mm/m' as main and secondary reinforcement.

Beam action (longitudinal direction):

P1=0.125*0.8*2.5+.35*1.5 = 0.8475t

P2 = 0.35 * 3 = 1.05 t

S1 = S2 = 0.79 t

| Plate | Width (m) | Height | Area (m2) | Z (m3) | S ( t/m') | M (m.t) | Stress (t/m2) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| ab | 0.125 | 0.80 | 0.1 | 0.0133 | 0.8475 | 42.4 | 3180.8 |
| bc | 0.12 | 3.0 | 0.36 | 0.18 | 0.79 | 39.5 | 219.44 |

Joint b:  0 + 2(Tb/A1+Tb/A2) + Tc/A2 = ½ (M1/Z1 + M2/Z2)

2*12.78 Tb = 1700.12 → Tb = 66.53t

Note:At Joint c Edge Shear = 0 because of the plate bc and cd compressed at same point (c)

Max. Compression stress = 100.65 kg/cm2 (safe)

T (tension force) = 0.5 * 185.1 * 0.6243 = 57.78 t

As = 57.78 / 2 = 28.89 cm2→12ø18mm

Shear stress

Max. Shear force at diaphragms Qmax = Pb L / 2 = 0.85 * 20 / 2 = 8.5 t

Shear stress at mid height of plate ab max = ³/² Qmax / A

= 3*8.5 /2*0.1 = 127.5 t/m2

Shear stress at diaphragms due to Tb = 66.5 t

At top edge  = 4Tb / b L =4*66.5/0.125*20 = 106.4 t/m2

At mid height /4 = 106.4 / 4 = 26.6 t/m2

Total shear stress at mid height = 127.5 – 26.6 = 101 t / m2

------------------------------------------------------------------------

Max. Shear force at diaphragms Qmax = Pb L / 2 = 0.79 * 20 / 2 = 7.9 t

Shear stress at mid height of plate bc max = ³/² Qmax / A

= 3*7.9 /2*0.36 = 33 t/m2

Shear stress at diaphragms due to Tb = 66.5t

At top edge  = 4Tb / b L =4*66.5/0.12*20 = 111 t/m2

At mid height /4 = 111 / 4 = 87.81 t/m2

Total shear stress at mid height of plate bc= -111 + 33 = -78 t / m2

Reinforcement for shear:

Design of Diaphragm:

Design each diaphragm as simply supported beam supported on columns.

Distributed loads acting on the diaphragm w /m' = o. wt. of diaphragm

+distributed load /m2 acting on plates * Span/2 =

8.0652*2.5*0.25/5.2+0.4*20/2

= 5 t/m'

Max. +ve Moment = 5*5.22/8 = 17 m.t.

Max. Shear Force = 5*5.2/2 = 13 t

Let the thickness of diaphragm = 25 cm

d = k1√M/b = 0.35√17*105/25 = 92 cm let d = 270 cm and t = 275 cm

As = M/k2 d = 17 * 105 / 2000 * 270 = 3.15 cm2 → 8 ø 18 mm

 = Q/0.87 bd = 50.4*1000/0.87*25*250 = 9.3 kg/cm2

Take 2*2 ø 18 mm as bent bars

Note:The reinforcement will cover the moment for small depth.

The bent bars will appear in the sloped depth section.

The secondary reinforcement for transfer direction resist shear stress in plates.